## Slide 1: Intelligent System and Robotics
Name : Sandeep Kumar Ramamoorthy
Registration Number : 2101119
Student Id : sr21990

## Slide 2: Controller design : P
Proportional controller
A controller that multiplies the tracking error by a constant 
ut = P * (rt -vt )
P affects
Transient response
Stability, oscillation
Steady state tacking
As large as possible
Disturbance rejection
As large as possible

## Slide 3: Controller design: PD
Proportional and Derivative control
ut = P * (rt -vt ) + D * ((rt -vt )-(rt-1 -vt-1 )) = P * et+ D * (et -et-1 )
Consider the size of error over time
Intuitively
Want to “push” more if the error is not reducing fast enough
Want to “push” less if the error is reducing really fast

## Slide 4: PD Controller
Need to keep track of error derivative
P can be set for best tracking and disturbance control
Then D set to control oscillation/overshoot/rate of convergence

## Slide 5: PI Cotrol
Proportional plus integral control
ut=P*et+I*(e0+e1+…+et )
Sum up error over time
Ensure reaching desired output, eventually
vss will not be reached until ess=0
Use P to control disturbance
Use I to ensure steady state convergence and convergence rate

## Slide 6: PID Controller
Combine Proportional, integral, and derivative control
ut=P*et+I*(e0+e1+…+et )+D*(et -et-1 )
Analytically deriving P, I, D may not be possible
E.g. plant not is not available, or to costly to obtain.

## Slide 7: Fuzzy Logic Controller
FL is a logical system, which is an extension of multivalued logic, where membership is a matter of a degree
Fuzzy Logic is a convenient way to map an input space to an output space. Mapping input to output is the starting point for everything.
Some ways to make the black box work: Fuzzy systems, linear systems, expert systems, neural networks, differential equations, etc.

## Slide 8: Fuzzy Logic
1. FL is conceptually easy to understand.
2. FL is flexible.
3. FL is tolerant of imprecise data.
4. FL can be built on top of the experience of experts.
5. FL is based on natural language, hence easy to use.

## Slide 9: Right edge following rule set
Right -front | Right-back | speed | steering
near | near | slow | left
near | medium | slow | left
near | far | medium | left
medium | near | medium | right
medium | medium | slow | zero
medium | far | medium | left
far | near | slow | right
far | medium | medium | right
far | far | fast | right

## Slide 10: obstacle avoidance rule set
Front-sensor | Left-sensor | Right-sensor | steering | speed
near | near | near | left | slow
near | near | medium | right | slow
near | near | far | right | slow
near | medium | near | left | slow
near | medium | medium | left | slow
near | medium | far | right | medium
near | far | near | left | slow
near | far | medium | left | medium
near | far | far | left | slow
medium | near | near | left | slow
medium | near | medium | right | slow
medium | near | far | right | slow
medium | medium | near | left | slow

## Slide 11: obstacle avoidance
Front-sensor | Left-sensor | Right-sensor | Steering | Speed
medium | medium | medium | left | slow
medium | medium | far | right | medium
medium | far | near | left | medium
medium | far | medium | left | medium
medium | far | far | right | medium
far | near | near | zero | slow
far | near | medium | right | slow
far | near | far | right | medium
far | medium | near | left | slow
far | medium | medium | zero | medium
far | medium | far | right | medium
far | far | near | left | slow
far | far | medium | left | medium
far | far | far | zero | fast